## Slide 1: Classification of Gender and Maturity Status in Chinook Salmon by Short Wavelength Near Infrared spectroscopy
Anna G. Cavinato, Calvin Davis, Heather Peters, Department of Chemistry, Eastern Oregon University,Tim Hoffnagle, Northeast Region Fish Research, Oregon Department of Fish and Wildlife, David M. Mayes, DSquared Development.
NWFCC, Portland, OR 2003

## Slide 2: Goals
Develop a means to classify fish according to their maturation status (immature or maturing) and gender at the earliest possible date.
Devise the method based on a non-invasive approach.

## Slide 3: SW-NIR Spectroscopy
Wavelength Region
    600-1100 nm
Overtone and Combination Bands of:
    O-H C-H N-H
Low Energy Electronic Transitions
    chlorophyll
    hemoglobin
    other highly conjugated systems

## Slide 4: Common SW-NIR Spectral Features

## Slide 5: Advantages of SW-NIR
Little or no sample preparation
Very short measurement time
Long path lengths (1-100 cm)
Non-destructive
Excellent signal to noise
Rugged instrumentation
Inexpensive fiber optics

## Slide 6: Comparison of scattering and absorbance in the NIR

## Slide 7
Disadvantages of SW-NIR
low sensitivity
  useful for components at concentrations > 1%
limited scope of functional groups
  absorption caused by C-H, N-H, O-H vibrations
absorption bands overlap
  instrument requires complicated calibration

## Slide 8
NIR Calibration - Multivariate Analysis
Classification methods:
  Principal Components Analysis (PCA)
  Soft Independent Modeling of Class Analogy (SIMCA)

## Slide 9: Fiber Optic Probe Design
Fiber Probe End
32 Illumination Fiber Optics
(600m)
1 Collection Fiber Optic
(600m)
Radius (2 mm)

## Slide 12: Spectra collection
170 spectra were collected at Bonneville in May 2002
750 spectra were collected at Manchester in March 2003
360 spectra were collected at Bonneville in April 2003
160 spectra were collected at Bonneville in June 2003

## Slide 13
Summary of SIMCA classification
Bonneville 2002
Probe Position | Base Pop. for Model | % correctly classified | % incorrectly classified
Belly 1(B1) | Mature Female | 79.40% 79.70% | 23.80% 38.50%
Belly 2 (B2) | Mature Female | 91.41% 80.39% | 9.10% 11.67%
Dorsal (D1) | Mature Female | 75.30% 77.20% | 42.90% 46.20%

## Slide 14: Spectra of eggs and testis

## Slide 15: PCA classification for eggs and testis

## Slide 16: Absorbance spectra of mature and immature fish
immature
mature

## Slide 17: 2nd derivative spectra of mature and immature fish
immature
mature

## Slide 22: Conclusions
SW-NIR spectroscopy shows great promise for classifying maturity and gender at early stages.
Experimental evidence confirms that light penetrates through skin and scales reaching gonadal tissues.
Approximately 100% immature fish can be correctly classified.
Results need to be validated with spawning observations.

## Slide 23: Acknowledgments
National SeaGrant College Program (Project #NA36RG0451/R/SF-13-PD)
Oregon Department of Fish and Wildlife
Confederated Tribes of the Umatilla Indian Reservation
Manchester Marine Laboratory
Bonneville Fish Hatchery
Eastern Oregon University
DSquared Development, Inc.